## Slide 1
S Raghunath
Professor, Department of Civil Engineering,
(NBA Accredited for 5 years : 2014-2019)
BMS College of Engineering, Bangalore 560019
Email: raghunath.smrc@gmail.com, raghu.civ@bmsce.ac.in
www.bmsce.ac.in
Performance of Masonry Structures During Earthquakes &
Concepts for Earthquake Resistant Masonry

## Slide 3
This figure was produced in cooperation with the US Geological Survey, and the University of Memphis private foundations
Local Magnitude - Seismic Energy correlation
Gujarat (2001)

## Slide 4
1819 Rann of Kutch earthquake
Allah Bund
The most dramatic effect of this earthquake was the formation of a ridge about 6 m high, extending for 80 km (possibly as much as 150 km) that formed a natural dam across the Puram river.
To distinguish it from the man-made dams that were common in the region, the uplifted area became known as the Allah Bund, or Dam of God.

## Slide 5
1897 Assam earthquake
Thought to have triggered 32 km below the surface, it left 390,000 sq. km of masonry buildings in ruins and was felt over 650,000 square kilometres from Burma to New Delhi

## Slide 8: Objectives
  Understand Structural Masonry
  Terminologies in Structural Masonry
  Masonry design concepts
  Behaviour of masonry structures during earthquakes – Performance and Failure modes
  Concepts for earthquake resistant masonry
  Design procedure for earthquake load analysis of masonry buildings

## Slide 9
 | Concrete | Masonry
Composition | Fine aggregate, coarse aggregate and binding material | Masonry units and mortar (fine aggregate and binding material)
Distribution of constituents |  | 
Behaviour |  | 

## Slide 10
 | Concrete | Masonry
Composition | Fine aggregate, coarse aggregate and binding material | Masonry units and mortar (fine aggregate and binding material)
Distribution of constituents |  | 
Behaviour |  | 

## Slide 11
 | Concrete | Masonry
Composition | Fine aggregate, coarse aggregate and binding material | Masonry units and mortar (fine aggregate and binding material)
Distribution of constituents |  | 
Behaviour | Good in compression, weak in tension, Brittle, Crack pattern is irregular Can be considered isotropic | Good in compression, weak in tension, Brittle, Cracks occur generally at unit-mortar interface, Orthotropic

## Slide 12
 | Concrete | Masonry
Reinforcement |  | 
For a civil engineer |  | 

## Slide 13
 | Concrete | Masonry
Reinforcement |  | 
For a civil engineer |  | 

## Slide 14
Advantages of Masonry
No formwork
Plays a dual role – functional and structural
Economy
Durable
Aesthetic
Can be made ductile
Can be made light-weight
Disadvantages of Masonry
Structurally very complex
Too many variables!

## Slide 15
Structural Walls have 3 functions:
Resist vertical compression
Resist out-of-plane bending from eccentric vertical loads (gravity loads), and/or transverse loads such as wind loads and earthquake loads
Resist in-plane forces (in-plane shear and in-plane bending) attracted by the masonry building as a whole

## Slide 16
Masonry is
Weaker than the brick
Weaker than the mortar (?)
Example
Block strength 40.0 N/mm2
Mortar type H1, strength 8.0 N/mm2
Masonry strength is only 3.05 N/mm2

## Slide 17
Typical “Masonry Prisms”

## Slide 18
Masonry Walls:
Slenderness and Eccentricity
Stocky wall, central load
100% strength
Slender wall, central load
Reduced strength

## Slide 19
Masonry Walls:
Slenderness and Eccentricity
Stocky wall, eccentric load
Reduced strength
e
Slender wall, eccentric load
Much more reduced strength

## Slide 20
Effective height
Effective length
Effective thickness
Eccentricity of load
Slenderness
Ratio
Stress Reduction Factors
Ult. load on wall x Factors (of safety)

## Slide 23
In un-reinforced masonry structures the lateral stability is provided by gravity.
No tension can be allowed to develop at the base of the structure. Hence un-reinforced masonry structures have to be sufficiently massive (large base width) so that the resultant of all forces acting on the structures does not fall outside the middle third of the base.

## Slide 24
Multi-storeyed Un-reinforced masonry tower, Tanjavur, India

## Slide 25
Un-reinforced masonry arches and aqueducts
(Ref: KS Jagadish and BP Sinha)

## Slide 38
Monadnock Building, Chicago, 1891
1.82m thick wall at basement!
(Ref: BP Sinha)

## Slide 39
Stability concept (Ref: BP Sinha)

## Slide 40
16 storeyed load bearing masonry
(Ref.: BP Sinha)

## Slide 41
18 storeyed load bearing masonry at Cleveland
(Ref.: BP Sinha)

## Slide 42
Stability concept, Atlintada Church designed by E. Dieste (Ref: BP Sinha)

## Slide 43: Reinforced Masonry
Un-reinforced load bearing masonry should be avoided since it is not entirely insulated from brittle modes of failure. This can be easily rectified by the usage of reinforced masonry.
Lesser unit weight when compared to massive URM
Eliminating the need for RC beams
Elimination of expensive form work which is otherwise required in conventional RC framed construction

## Slide 44: Reinforced masonry

## Slide 45: Reinforced/Pre-stressed masonry

## Slide 46: Reinforced/Pre-stressed masonry

## Slide 47
ANTONIO GAUDI – LA PEDRERA

## Slide 48
ANTONIO GAUDI – CRYPT OF THE GUELL INDUSTRIAL VILLAGE

## Slide 49: CORBELLED ARCH (ANTONIO GAUDI)

## Slide 50: 9 STOREYED HOTEL – NASHIK - LOAD BEARING MASONRY BUILDING. - HOLLOW CONCRETE BLOCKS.

## Slide 51
Factors:
Effective height of wall
Effective length of wall
Effective thickness of wall
Eccentricity of load
To be chosen:
Strength of brick or block
Type of mortar
Load on wall, kN/m

## Slide 52
Masonry is
Weaker than the brick
Weaker than the mortar (?)
Example
Block strength 40.0 N/mm2
Mortar type H1, strength 8.0 N/mm2
Masonry strength is only 3.05 N/mm2

## Slide 53
Typical “Masonry Prisms”

## Slide 54
Masonry Walls:
Slenderness and Eccentricity
Stocky wall, central load
100% strength
Slender wall, central load
Reduced strength

## Slide 55
Masonry Walls:
Slenderness and Eccentricity
Stocky wall, eccentric load
Reduced strength
e
Slender wall, eccentric load
Much more reduced strength

## Slide 56
Effective height
Effective length
Effective thickness
Eccentricity of load
Slenderness
Ratio
Stress Reduction Factors
Ult. load on wall x Factors (of safety)

## Slide 57
Stress reduction factors as per IS 1905

## Slide 58
Capacity reduction factors as per BS 5628

## Slide 59
Capacity reduction factors as per EURO Code

## Slide 61
Structural Walls have 3 functions:
Resist vertical compression
Resist out-of-plane bending from eccentric vertical loads (gravity loads), and/or transverse loads such as wind loads and earthquake loads
Resist in-plane forces (in-plane shear and in-plane bending) attracted by the masonry building as a whole

## Slide 64
Summary:
Masonry is the most simplest load bearing system. The walls are ‘constructed’ to remain ‘stable’. Having ensured ‘stability’, the load carrying capacity is then checked.
As ‘slenderness’ and ‘eccentricity’ of applied vertical load increases, the load carrying capacity reduced significantly.
In case of un-reinforced masonry, it is to be ensured that ‘tensile stresses’ do not develop in any of the walls because masonry is very brittle, particularly in tension.

## Slide 65
Earthquake Protection
(Coburn and Spence, 2002)

## Slide 66
Grade 1: Negligible to slight damage (no structural damage)

## Slide 67
Grade 2: Moderate damage (slight structural damage, moderate non-structural damage)Large and extensive cracks in many walls; parts of chimneys fall down.

## Slide 68
Grade 3: Substantial to heavy damage (moderate structural damage, heavy non-structural damage);large and extensive cracks in most walls; pan tiles or slates slip off; chimneys are broken at roof line; failure of individual non-structural elements.

## Slide 69
Grade 3: Substantial to heavy damage (moderate structural damage, heavy non-structural damage);large and extensive cracks in most walls; pan tiles or slates slip off; chimneys are broken at roof line; failure of individual non-structural elements.

## Slide 70
Grade 4: Very heavy damage(heavy structural damage, very heavy non-structural damage);serious failure of walls; partial structural collapse.

## Slide 71
Grade 5: Destruction (very heavy structural damage) ; Total or near total collapse.

## Slide 80
September 30, 1993 Latur earthquake….

## Slide 82
Out-of-plane collapse of sandstone in lime mortar masonry wall (MORBI)

## Slide 83
House with lintel band and columns (SAMAKHYALI)

## Slide 84
Combination of in-plane and out-of-plane failure (Samakhyali)

## Slide 85
Separation of corner column from the neighbouring masonry (SAMAKHYALI)

## Slide 86
Stone masonry building in CM – minor damage(BHUJ)

## Slide 87
Out-of-plane failure of wall leading to collapse of lintel band (BHUJ)

## Slide 88
Corner failure in presence of corner reinforcement (BHUJ)

## Slide 89
Collapse of walls between openings (KHAVDA)

## Slide 90
Rigid box like behaviour above lintel band (BHACHAU)

## Slide 91
Shear cracks in stair-case room of a school bldg. (Morbi)

## Slide 92
Damage due to a combination of in-plane and
out-of-plane vibration (Samakhyali)

## Slide 93
Out-of-plane collapse of stair case room of a school building (Morbi)

## Slide 94
Wall flexure – RC roof on stone-in-CM (Lodhrani)

## Slide 95
Vulnerability of parapets and other projections (Morbi)

## Slide 96
Vulnerability of light-roofed masonry house (Khavda)

## Slide 98
Out-of-plane failure and buckling of wythes

## Slide 99
Vulnerability of heavy-roofed masonry house

## Slide 100
Haiti earthquake (2010)

## Slide 101
Vulnerability of masonry, Haiti earthquake (2010)

## Slide 102
Summary of types of masonry building damages/failures
Out-of-plane collapse and or shear failure
In-plane shear and or flexure failure
Separation of wall junctions
Failure of masonry pier in between openings
Local failures
Buckling of wythes
Separation of roof from walls

## Slide 103
EARTHQUAKE RESISTANT MASONRY

## Slide 106
TURKEY

## Slide 107
TURKEY

## Slide 108
UTTRAKHAND

## Slide 109
UTTRAKHAND

## Slide 110
UTTRAKHAND

## Slide 111
HIMACHAL PRADESH

## Slide 112
HIMACHAL PRADESH

## Slide 117
Response of structures during earthquake depends on
Natural frequencies of the structure (which is dependent on Mass (M) and Stiffness (K)
Frequency content of earthquake
Amplitude of earthquake
Duration of earthquake
Ductility
Damping characteristics (energy dissipation capacity)
Structural integrity

## Slide 118
EIGEN values
Natural frequencies
EIGEN vectors
Mode shapes

## Slide 119
period range of masonry buildings

## Slide 120
QUASI-STATIC
RESONANT
INERTIAL

## Slide 121
building without roof,
without opening (B*)
(b) building without roof,
with opening (B*O)
(c) building with roof,
without opening (B*R)
(d) building with roof,
with opening (B*OR)
Fig. – 4.5: Building configuration chosen for parametric study

## Slide 122
Figure 1: Buildings without roof (a) without bands (b) with RC lintel and roof bands
(a)
(b)
Figure 2: Building with RC roof and lintel band
Cross wall
Shear wall

## Slide 123
Fundamental mode shape of building without roof, with openings

## Slide 124
Fundamental mode shape of building with roof and openings

## Slide 125
Parameters of wall analysis
Base
Vertical edge
Vertical edge
x
y
mid-height
mid-length
4m, 6m and 9m
3.0m

## Slide 126
S S C F boundary condition for the 4 edges of the wall

## Slide 127
S S C S boundary condition for the 4 edges of the wall

## Slide 128
STRESSES IN MASONRY WALLS DURING EARTHQUAKE GROUND MOTIONS

## Slide 129
STRESSES IN MASONRY WALLS DURING EARTHQUAKE GROUND MOTIONS

## Slide 130
 (parallel-to-bed-joints) Strength: < 0.36 MPa

## Slide 131
 (normal-to-bed-joints) Strength: < 0.10 MPa

## Slide 132
Regions of maximum flexural stress for buildings without roof (a) σx (b) σy

## Slide 133
Regions of maximum flexural stress for buildings with roof (a) σx (b) σy

## Slide 134
Regions of maximum shear stress in shear-walls (t)

## Slide 135
Out of plane flexural collapse

## Slide 136
Typical X-type crack

## Slide 137
TYPE OF EQ. | CRITERION
MILD | Frequent occurrence NO STRUCTURAL DAMAGES ADMISSIBLE, NON-STRUCTURAL DAMAGES ALLOWED BUT REPAIRABLE
MODERATE | May occur once during the life-time of a structure ALLOW MINOR BUT REPAIRABLE STRUCTURAL DAMAGES
MAJOR | Very rare possibility MAJOR STRUCTURAL DAMAGE ALLOWED, BUT STRUCTURE SHOULD NOT COLLAPSE
DESIGN PHILOSOPHY

## Slide 138
Design Principles
Achieve strength and ductile behaviour
Maintain structural integrity
In relatively simple and cost effective manner!

## Slide 139
Different ways of reinforcing masonry
Horizontal reinforcement
Vertical reinforcement
Core reinforcement
Containment reinforcement (Surface reinforcement)

## Slide 140
IS 4326 – 1993 (re-affirmed 1998), “Earthquake resistant design of buildings – codes of practice”, BIS, New Delhi

## Slide 141
IS 4326 – 1993 (re-affirmed 1998), “Earthquake resistant design of buildings – codes of practice”, BIS, New Delhi

## Slide 146
EARTHQUAKE RESISTANT MASONRY CONCEPTS
Traditional / Innovative practices
Turkey – Horizontal timber scantlings on either face – 3 levels per floor
Quetta, Kutch – Horizontal and vertical railings with brick in-fill
Horizontal expanded metal every fourth course
Uttarkashi – Horizontal timber bands at different levels

## Slide 147
Ref: Tomazevic
Horizontal RC bond beams at 1.0 or 2.0 m spacing
Masonry confined by RC framing, walls keyed to frame
Vertical reinforcement in grouted hollow block masonry
Horizontal steel ties below floor level
Reinforced cement coating (M P Jaisingh)
Ref: Gavrilovic & Ginell
Horizontal RC bond beams, vertical nylon straps on both faces

## Slide 149
IS 4326 – 1993 (re-affirmed 1998), “Earthquake resistant design of buildings – codes of practice”, BIS, New Delhi

## Slide 151
Vertical reinforcement
Very difficult to provide, especially for masonry with solid blocks
Needs to be grouted by rich mortar/concrete
Provides good shear resistance
Closely spaced vertical reinforcement with grouting may increase the stiffness

## Slide 156
IS 4326 – 1993 (re-affirmed 1998), “Earthquake resistant design of buildings – codes of practice”, BIS, New Delhi

## Slide 162
(a) Un-reinforced (b) core-reinforced (c)Containment reinforcement

## Slide 163
Reinforcement on both faces to be held by ties going through the wall in alternate courses or once in 3 courses
Following materials are possible
    GI wire – 3.0 to 4.0 mm
    Corrosion resistant steel ~ 6.0mm
    Stainless steel – 3.0 to 4.0 mm
    Bamboo
    Timber
Function is to prevent growth of flexural cracks
Experiments show good flexural ductility

## Slide 164
1st crack

## Slide 170
b
h
δs
(a) In-plane pure shear

## Slide 171
b
h
δs
F
b
h
F
δbbb
(b) In-plane shear + bending (fixed-fixed)

## Slide 172
b
h
δs
b
h
F
δbc
F
(c) In-plane shear + bending (cantilever)

## Slide 173
Torsion stiffness of shear wall
Torsion stiffness of cross wall

## Slide 185
Shear force distribution along the height (storey shear)

## Slide 186
Bending moment distribution along the height

## Slide 190
Calculation of Geometric Properties:
Pier Areas (cross sectional)
Area of Pier 1 = (800×190+1000×190) = 3.42×105 mm2
Area of Pier 2 = (1000×190) = 1.9 ×105 mm2
Area of Pier 3 = (800×190+1000×190) = 3.42×105 mm2

## Slide 191
Height of pier 1 = 1.2 m
Height of pier 2 = 1.2 m
Height of pier 3 = 2.8 m
Em = 550×fm’ = 550 x 8.0 = 4400 MPa

## Slide 193
Stiffness k1 = 1.855 x 105 N/mm
Stiffness k2 = 1.569 x 105 N/mm
Stiffness k3 = 4.294 x 105 N/mm

## Slide 194
Distribution of Lateral Shear among Piers:
As the floor is assumed to be rigid the lateral forces will be distributed in proportion to the pier stiffness.
Ve = Vb x relative stiffness
= Vb x stiffness of each pier/total stiffness
Total base Shear = (40 + 40+20) = 100 kN

## Slide 196
Pd = Axial load due to Dead load
Pl = Axial load due to live load
Pe = Axial load due to Moment (M = Pe/Z) overturning
Ve = Lateral load (shear force)
Me = Ve x h/2 (assuming fixed-fixed condition at top and bottom of walls/piers)

## Slide 199
Basic properties of bricks, blocks and mortar
Basic properties of masonry bricks
Dimensionality test
Dry density test
Water absorption test
Initial Rate of Absorption
Compressive strength
Tensile strength
Flexural strength
Modulus of elasticity

## Slide 200
Compressive strength of Masonry Prisms (fm’)
S Raghunath, BMSCE, Bangalore 19

## Slide 201
Various types of shear tests

## Slide 202
Triplet Shear test

## Slide 203
Diagonal split tension test (in-direct shear test)

## Slide 204
Flexure test

## Slide 205: Summary of topic
  Understand Structural Masonry
  Terminologies in Structural Masonry
  Masonry design concepts
  Behaviour of masonry structures during earthquakes – Performance and Failure modes
  Concepts for earthquake resistant masonry
  Design procedure for earthquake load analysis of masonry buildings

## Slide 208
Model 1
(ERF as per
IS 4326:1993)
Model 2
(ERF as per
IS 4326:1993
plus additional
R C band at
Sill level and
Containment
reinforcement

## Slide 211
Corner failure (Bhuj)
Corner failure (Lab Model)

## Slide 212
Failure of masonry below lintel band (Bhuj)
Failure of masonry below lintel band (Lab model)

## Slide 213: Technology Dissemination in Gujarat Courtesy NCPDP, Nirma University and Prof. KSJ and SR

## Slide 218: Development of Reinforced Masonry at BMSCE
Masonry building with horizontal bands and ‘Containment reinforcement’ – VTU sponsored R&D project

## Slide 219
Building Model - Dome

## Slide 220
Testing – Crack Patterns in walls
West Wall of Prototype Model

## Slide 221
Concluding comments….
Learn
Educate
Implement
Improve
..
..

## Slide 222: Contact
S Raghunath
Professor, Department of Civil Engineering
BMS College of Engineering
Phone: +91 80 98457 94060
email: raghunath.smrc@gmail.com
raghu.civ@bmsce.ac.in
Web: www.bmsce.ac.in
THANK YOU

## Slide 223
S Raghunath, BMSCE, Bangalore 19